## Slide 1: THE HITCHHIKER’S GUIDE TO STEEL BRIDGE DESIGN
A BRIEF INTRODUCTION

## Slide 2: PROJECT TASKS
Order Steel
Rules Released
Fundraising
Design
Fabrication
Construction Practice
Mid-Pac
Recruitment & Fabrication Training
Fall Quarter
Begins
Design Training

## Slide 3: GANTT CHART
2±1m
2±1m
3±1m
FALL
WINTER
SPRING
SUMMER
Fundraising
Design Training
Design
Order Steel
Fabrication
Construction
Mid-Pac
Fall Quarter Begins
Rules Released
Recruitment
2±1w
2±1w
3±1m
4±1w

## Slide 4: CRITICAL TASKS
Order Steel
Rules Released
Fundraising
Design
Fabrication
Construction Practice
Mid-Pac
Recruitment & Fabrication Training
Fall Quarter
Begins
Design Training

## Slide 5: CRITICAL TASKS
Order Steel
Rules Released
Fundraising
Design
Fabrication
Construction Practice
Mid-Pac
Recruitment & Fabrication Training
Fall Quarter
Begins
Design Training

## Slide 6: DESIGN KNOWLEDGE/SKILLS
Drafting (AutoCAD)
  drafting proficiency (ECI 16)
Structural Analysis (SAP2000, SolidWorks)
  knowledge of mechanics (ENG 104, ECI 130)
  familiarity with structural modeling (ECI 131)
  understanding of steel failure mechanisms (ECI 132)
Programming & Optimization (MATLAB, Excel)
  proficiency with Excel functions, macros
Fabrication & Construction experience
  knowledge of available tools, practical limitations
  “design for manufacturability” (DFM)
NSSBC Rules

## Slide 7: DESIGNERS OF THE PAST
2010-2011: DQ’ed at Mid-Pac
  Designed by Suppayarn Dechpormsuk
2011-2012: 7th place nationally
  Designed by Alex Wong
2012-2013: 3rd place nationally
  Designed by Brian Giffin
2013-2014: 1st place nationally
  Designed by Quincy Dahm
2014-2015: 16th place nationally
  Designed by Jennifer Yasui

## Slide 8: DESIGNERS OF THE PAST
2010-2011: DQ’ed at Mid-Pac
  Designed by Suppayarn Dechpormsuk (team captain)
2011-2012: 7th place nationally
  Designed by Alex Wong (team captain)
2012-2013: 3rd place nationally
  Designed by Brian Giffin (team captain)
2013-2014: 1st place nationally
  Designed by Quincy Dahm (team captain)
2014-2015: 16th place nationally
  Designed by Jennifer Yasui (team captain)
Captain and designers (both/one in the same) require broad knowledge & skills to be effective

## Slide 9: ITERATIVE DESIGN WORKFLOW
Drafting
Model Setup
Analysis
Evaluation
Revision
Member Resizing
Design Constraints
Optimal Design
Full workflow demonstrated in “Design Tutorials”

## Slide 10: DESIGN CONSTRAINTS
Rules:
Dimensional limitations (overall, members)
Connection type prohibitions (2013, 2014)
Fabrication:
Tubing size and material selection limitations
Design complexity/tooling limitations
Construction:
Assembly order
Bolt placement/clearances
Failure:
Material yielding, fracture, buckling & stability

## Slide 11: DRAFTING
In AutoCAD:
Specify design space
Sketch conceptual design
Draw frame sections using named layers
Assess member dimensional constraints
Try to spend more of your time designing here
(explore more design alternatives)

## Slide 12: MODEL SETUP
In SAP2000:
Import geometry from AutoCAD
Assign model restraints (supports)
Define materials and cross-sectional properties
Assign frame sections to model members
Define loading cases
Specify deflection measurement points
Try to spend minimal amount of time doing this
(repetitive, time-consuming, error-prone)

## Slide 13: ANALYSIS
In SAP2000:
Run analysis…
That’s it!
(commercial analysis software is fairly fast!)

## Slide 14: EVALUATION
In SAP2000 and Excel:
Check for failure/violation of constraints
Check for structural instabilities
Query weight and deflections from model
Approximate construction costs
Compute the estimated overall cost/score
Compare against competing designs
Try to spend minimal amount of time doing this
(repetitive, time-consuming, error-prone)

## Slide 15: MEMBER RESIZING
In SAP2000:
Determine critically stressed members
Resize failing members for strength
Look at flexible members carrying high loads
  Increase tubing sizes to increase stiffness
Look at heavy members carrying low loads
  Decrease tubing sizes to reduce weight
Historically, consumes most of the design time
(combinatoric optimization problem)

## Slide 16: REVISION
In AutoCAD:
Determine major design issues
Target sources of inefficiency
Devise structural improvements
Requires the most engineering judgment
(use your intuition and logical reasoning)

## Slide 17: OTHER CONSIDERATIONS
Beyond minimizing the overall score, consider:
Actual cost (budgeting, time constraints)
Ease, speed, accuracy of fabrication (DFM)
  Simpler fabrication => fewer fabrication errors
  Faster fabrication => more construction practice
  Better quality fabrication => easy/fast assembly
Tolerances for error (use a factor of safety!)
  Failure, dimensional limitations, lateral deflection
Ease of assembly (connection design)
  Require fewer builders; faster construction

## Slide 18: OPTIMAL STOPPING

FALL
WINTER
SPRING
SUMMER
Fundraising
Design Training
Design
Order Steel
Fabrication
Construction
Mid-Pac
Fall Quarter Begins
Rules Released
Recruitment



Finishing early yields extra “slack-time,” but design may be less optimized; limited by funding/training

## Slide 19: OPTIMAL STOPPING


FALL
WINTER
SPRING
SUMMER
Fundraising
Design Training
Design
Order Steel
Fabrication
Construction
Mid-Pac
Fall Quarter Begins
Rules Released
Recruitment


Optimal timing coincides with steel arriving at the end of the recruitment/fabrication training period

## Slide 20: OPTIMAL STOPPING
FALL
WINTER
SPRING
SUMMER
Fundraising
Design Training
Design
Order Steel
Fabrication
Construction
Mid-Pac
Fall Quarter Begins
Rules Released
Recruitment




Finishing design too late leaves little or no time for construction practice! (may also affect fabrication)

## Slide 21: DESIGN BOTTLENECKS
Designing “by hand” is prohibitively slow:
Model setup phase stymies exploration of alternative designs, structural modifications
  SAP GUI is cumbersome, repetitive, error-prone
Evaluation phase also repetitive, error-prone
  Effort scales with the number of design iterations
Member resizing is an intractable problem
  (400+ members)x(150+ tubing sizes)x(N designs)
  Try to make well-informed sizing selections

## Slide 22: AUTOMATED DESIGN TOOLS
Drafting
Model Setup
Analysis
Evaluation
Revision
Member Resizing
re.STRUCT
AutoCAD
proto.BRIDGE
SAP2000
fore.SCORE
Essential paradigm: wherever possible, automate repetitive and time-consuming tasks
You!
Tools showcased in “Technical Demonstrations”

## Slide 23: APPLICATION PROGRAMMING INTERFACE (API)
Most commercial software allows users to interact with a program through an “API”
Any GUI operation can be performed through a corresponding API call
AutoCAD API: for C++, Python, VB.NET (VBA)
SAP2000 OAPI: for VBA, Matlab, Python
MS Excel: Good platform for VBA development
Repetitive interactions can be fully automated
Complicated interactions are made possible

## Slide 24: proto.BRIDGE
Automates model setup process
Originally written for Excel VBA
Uses APIs to convert AutoCAD drawings directly into analysis-ready SAP2000 models
Places some restrictions on drawing format
Requires model parameter definitions within the accompanying Excel spreadsheet:
  restraints, sections, loads, deflection locations

## Slide 25: fore.SCORE
Automates design evaluation process (mostly)
Originally written for Excel VBA
Uses SAP’s OAPI to query model weight and deflections for all loading cases
Excel spreadsheet computes and tabulates overall score history for design comparisons
Uses SAP’s built-in “Steel Design Checks” to check for failing members (insufficient)
Currently does not run buckling analyses

## Slide 26: re.STRUCT
Automates member resizing (work-in-progress)
Originally written for Excel VBA
Uses SAP’s OAPI to query member stresses and failure states
Performs non-linear iterations to determine optimal member section sizes
Selection criteria driven by cost functional minimization (may warrant discussion)
Tends to converge toward “local minima”

## Slide 27: GUIDED SETUP
What you’ll need:
SAP2000 v15 (or later)
AutoCAD 2013 (or later; non-student version)
MS Excel 2007 (or later)

## Slide 28: POTENTIAL TOPICS
Optimization theory
  Discuss the inner-workings of re.STRUCT
  Explore opportunities for shape optimization
Introduction to programming in Visual Basic
  Common VBA functions and data objects
  Invoking API functions
Connection design
  Fabrication considerations & constraints (DFM)
  Finite element stress analysis methods

## Slide 29: QUESTIONS?

## Slide 30: LEVELS OF OPTIMIZATION
Topology Optimization
  Member/joint connectivity
Shape Optimization
  Joint placement
Member Optimization
  Member section sizing
Generality,
Global Optimum
Practicality,
Diminishing Returns

## Slide 31: OPTIMIZATION HIERARCHY
Converge to an optimal topology
  Over-truss or under-truss?
  Topology directly influences construction cost
  Most major design choices made at this stage
  Start planning a fabrication schedule early on
Converge to an optimal shape
  Joint positioning, lateral placement, webbings
Converge to optimal member section sizes
  Controls the connection design